## Slide 1: Computer Architecture
Prof. Saurabh Gandhi (EEE department)

## Slide 2: Instructions as seen by hardware

## Slide 3: The 6 basic RV32I instruction formats – R, I, S, B, U, J

## Slide 4: General structure of instructions
opcode (7 bits): operation code, what operation to perform
rd (5 bits): destination register, for the result of the operation
rs1, rs2 (5 bits each): source registers, or operands
funct3 (3-bit), funct7 (7-bit): refine operation
imm: immediate, directly provide a literal value

## Slide 5: R-format instructions
opcode: instruction class (e.g., integer ALU)
funct3: selects ALU operation group
funct7: refines operation (e.g., add vs sub)

## Slide 6: I-format instructions

## Slide 7: Notice any quirks?
What happened to func7 in I-type arithmetic?
Why not use the same encoding logic for operation?
I-types prefer more bits for Imm
Why not remove func7 from R-type also?
Fewer R-type instructions supported (currently 10 R-type instructions, so 3 func3 bits insufficient)
I-type does not have subi (and jugglery for shifts)
Hierarchical decoding – next class!

## Slide 8: S-format instructions
More quirks!
Why is imm split?
Prefer rs1, rs2, rd (whenever required) in the fixed locations – simplifies decoding circuit

## Slide 9: Full picture
Opcode (binary) | Opcode (hex) | Instruction Class | Format(s) | Role of funct3 | Role of funct7
0110011 | 0x33 | Integer register–register ALU | R-type | Selects ALU operation group (ADD/SUB, AND/OR, shifts, SLT) | Distinguishes operations sharing same funct3 (e.g., ADD vs SUB, SRL vs SRA)
0010011 | 0x13 | Integer register–immediate ALU | I-type | Selects immediate ALU operation (ADDI, ANDI, ORI, shifts) | Used only for shift immediates (slli, srli, srai)
0000011 | 0x03 | Loads | I-type | Selects load width (lb, lh, lw, etc.) | Not used
0100011 | 0x23 | Stores | S-type | Selects store width (sb, sh, sw) | Not used
1100011 | 0x63 | Conditional branches | B-type | Selects comparison type (beq, bne, blt, bge, etc.) | Not used
1101111 | 0x6F | Jump and link | J-type | Not used | Not used
1100111 | 0x67 | Jump and link register | I-type | Fixed (000) | Not used
0110111 | 0x37 | Load upper immediate | U-type | Not used | Not used
0010111 | 0x17 | Add upper immediate to PC | U-type | Not used | Not used
1110011 | 0x73 | System / CSR | I-type | Selects CSR operation | Further refines system behavior

## Slide 10: Review questions
Two possible designs of 3-to-8 decoders:
A B

## Slide 11: Microarchitecture – datapath

## Slide 12: How is an instruction executed?
Goal: Create a “circuit” of logic elements that, when given an assembly instruction, perform the action the instruction describes

## Slide 13: The stages of instruction execution – Instruction Fetch (IF)
Which instruction to fetch? Logical elements to compute the address of the next instruction
Next instruction – easy, just increment the current instruction address by size
Branch – depends on the outcome of the current instruction (information obtained from other units of the processor

## Slide 14: The stages of instruction execution – Decode and Operand Fetch (OF)
How to interpret the instruction? What all will be needed to execute it?
Processing required for different instruction types is very different – load-store instructions use a dedicated memory unit, whereas arithmetic instructions do not
Notes: R-type: register-register.
I-type: short immediates and loads.
S-type: stores.
B-type: conditional branches, a variation of S-type.
U-type: long immediates.
J-type: unconditional jumps, a variation of U-type.

## Slide 15: The stages of instruction execution – Execute (EX)
Executes arithmetic and logical operations
Contains an arithmetic and logical unit (ALU)
Compute the effective address of load-store operations
Computes the outcome of branches

## Slide 16: The stages of instruction execution – Memory Access (MA)
Processing load-store instructions (accessing main memory)
Memory system can be very complex, and part of that complexity is implemented here (next module!)

## Slide 17: Data and control path
Datapath: contains the hardware necessary to perform operations required by the processor Reacts to what the controller tells it! (ie. “I was told to do an add, so I’ll feed these arguments through an adder)
Control: decides what each piece of the datapath should do What operation am I performing? Do I need to get info from memory? Should I write to a register? Which register? (Based on the input instruction!)

## Slide 18: The final product – virtual

## Slide 19: The final product – physical!
https://twitter.com/ten_filip/status/1340400266047332354
https://eater.net/8bit
Try your own: https://hackaday.io/project/178826-pineapple-one/details

## Slide 20: Components of the datapath

## Slide 21: What hardware blocks does an instruction use?
Program memory – where the instructions come from
PC – register that points to the instruction in memory
Register File – where the local registers live
Immediate generator
ALU – where the computation happens
Data memory

## Slide 22: The RV32I Register File
32 integer registers, x0 to x31
  Output ports portA and portB (readout of 32 bit data stored inside)
  Input port portW (32 bit data that we want to write inside)
  RW, RA, RB (address of register inside the RF resp.)
  WEn (whether to copy portW data into register inside or not)
  Clk (clock signal for write operation, read is combinational)!
Register x0 is hardwired to 0 (why?)
General purpose usage (ie registers are not restricted or reserved for specific uses)

## Slide 23: Immediate generator
Immediates are weirdly scattered
Immediates are not 32-bit (but ALU requires 32-bit inputs)
What ImmGen does:
  Reassemble bits
  Sign extend
  (+74) 01001010  0000000001001010
  (-74) 10110110  1111111110110110
  Alignment (for branching and jumping)
  00000001000 (11 bits)  000000010000 (12 bits)

## Slide 24: The ALU
Performs arithmetic (ADD, SUB) and logical (AND, OR, XOR) operations
Inputs:
  two 32-bit values + 4-bit ‘operation select’
Outputs:
  32-bit result + ‘zero’ flag
Which instructions would use the ALU?

## Slide 25: Program counter
Address of current instruction
Updated every instruction
PC  PC + 4
PC  PC + offset (branch)
PC  target address (jump)

## Slide 26: Instruction and data memory
Memory (idealized)
One input port: Data In
One output port: Data Out
Memory access:
Read: Write Enable = 0, data at Address is placed on Data Out
Write: Write Enable = 1, Data In written to Address
Clock input (CLK)
CLK input is a factor ONLY during write operation
During read, behaves as a combinational logic block: Address valid → Data Out valid after “access time”

## Slide 27: Control – one circuit to rule them all

## Slide 28: Instruction decode and control

## Slide 29: Instruction Fetch (IF) has fetched 32 bits of an instruction
Now what?
Instruction decode
Extract different fields from the instruction
Generate control signals that activate appropriate datapath components
Generate immediate
Every instruction is decoded, so strongly affects timing and power!

## Slide 30: Control- and data- relevant bits
Control relevant information:
Opcode
Func3
Func7
Data-relevant information:
rs1, rs2, rd
immediate

## Slide 31: What all does Control control?
Write to register file? RegWrite
Register writes from ALU result or memory? MemToReg
Write to data memory? MemWrite
ALU – what operation to perform? ALUop
ALU – what inputs to select (register or immediate)? ALUSrc
  Muxes
PC – +4 or new? PCSel

## Slide 32: Bit slicing – extracting instruction fields
32-bit bus split into dedicated wires with downstream connections
Data relevant bits
  Register file address inputs
  Immediate generator inputs
Control relevant bits
  Main control unit to decide what signals to generate

## Slide 33: Hierarchical decoding of control bits
Decoding the opcode
  0110011: R-type
  0010011: I-type
  0000011: Load
  1100011: Branch
If opcode says R-type, Main Control knows it has to set RegWrite = 1 (ie write back is surely involved)
Lets ALU Control decide what operation to perform
Main Control smaller and faster
ALU Control only if required by the instruction

## Slide 34: Instruction class based control

## Slide 35: ALU Control
Main Control sends 2-bit signal to ALU (ALUop)
  00: Force ADD (for load/store instructions)
  01: Force SUB (for branch comparisons)
  10: Use func3 and func7 to decide operation
ALU decoder / control:
  Inputs: ALUop, func3, func7
  Output: 4-bit ALU operation select

## Slide 36: ALU Control

## Slide 37: Decode Walkthrough: add x5, x3, x4
Opcode → ALU instruction
funct3 = 000 → add/sub group
funct7 = 0000000 → ADD
Control signals:
  read rs1, rs2
  select ALU add
  enable register write
  PC ← PC + 4

## Slide 38: Decode Walkthrough: lw x5, 8(x10)
Opcode → load class
funct3 = 010 → word load
Immediate generation enabled
Control signals:
  ALU computes address memory
  read enabled
  register write enabled

## Slide 39: Building a datapath for R-type instructions
Let us work with an example instruction: add t0 t2 t3
What steps do you need to execute? Remember we had a list of 5 steps:
1. Fetch: add t0 t2 t3
2.1 Decode: rd = t0; rs1 = t2; rs2 = t3
2.2 Operand fetch (read data): R[t2] R[t3]
3. Execute (perform operation): R[t2] + R[t3]
5. Write results back into register: R[t0] = R[t2] + R[t3]

## Slide 40: Implementing R-type instructions
Instruction fetch
  PC contains instruction address
  Connect to IMEM input (address bus)
  How is PC updated after the instruction? PC PC + 4
  Instruction appears on IMEM data bus
Decode / operand fetch
  Slice register address fields and connect to RegFile address input
  Corresponding data appears at output of RegFile
Execute
  Operands provided to ALU
  What operation to perform?
Control signals!
  Control unit receives opcode, func3 and func7
  Generates ALUSel (or ALUOp)
Writeback
  Another control signal to enable RegWrite

## Slide 41: Adding I-type arithmetic instructions to the datapath
1. Fetch: addi t0 t2 28
2.1 Decode (parse the instruction and extract different fields): rd = t0; rs1 = t2; rs2 = t3; imm
2.2 Operand fetch (read data): R[t2] R[t3] imm
3. Execute (perform operation): R[t2] + R[t3] + imm
5. Write results back into register: R[t0] = R[t2] + R[t3] + imm
Notes: What does ImmSel do?
What does BSel do?

## Slide 42: Adding I-type load instructions to the datapath
Do we need to change hardware, control, or both?
Can we fetch our instruction?
  YES!
Can we decode our instruction?
  YES!
Can we select the operands we need?
  YES! (still R[rs1] and immediate)
Do we have support for the operation we’re performing?
  YES! (ALUSel = Add)
Can we access memory?
  Need to add one!
Anything else needs to be changed?
  Register writeback needs to come from DMEM not ALU output!

## Slide 43: Adding S-type (store) instructions to the datapath
What do we need to change to support storing?
Do we need to update R[rd]?
  No! Stores don’t write back to register file!
  Need a new control bit
What gets stored in DMEM?
  R[rs2]

## Slide 44: What kinds of instructions are still remaining?
Change program flow: Jumps and branching!
What key features do they require?
Modify the PC
Done: R-type arithmetic, I-type arithmetic, I-type load and I-type store
Modify registers Modify memory

## Slide 45: Implementing branches
What operations do we need for branching?
Comparison (R[rs1] == R[rs2])
Addition (PC = PC + Imm)
Do we have the required hardware already?
Our ALU can do one of these, but not both! We need to add more hardware!
BrEq = 1, if A=B
BrLT = 1, if A < B
BrUn = 1 selects unsigned comparison for BrLT, 0 = signed
“Output” control signals are used to set other controls!
How many more muxes do we need to complete the datapath for beq support?

## Slide 46: Implementing jumps
JALR rd, rs, immediate
How many operations do we need to perform?
Do we need more hardware to implement them, like beq?
Write PC+4 to Reg[rd]
  Change writeback mux to accommodate another source
PC = Reg[rs1] + immediate
Uses same immediates as arithmetic and loads
  no multiplication of imm by 2 for alignment (for jalr)
Should we skip alignment?
How do we ensure alignment?
No!
Mask bit 0!

## Slide 47: The entire RISC-V RV32l datapath

## Slide 48: The control logic
Is control logic combinational or sequential?
Control signals do not depend on previous state!
Hierarchical:
Level 1: opcode based (instruction class)
Higher levels: func3, func7

## Slide 49: The control truth table

## Slide 50: Implementing control logic
Combinational hardwired logic
Programmable (ROM / PLA based)
What are the trade-offs?
Combinational:
  Hardwired, so cannot be modified
  Less expensive
Programmable:
  Fix errors
  Add new instructions

## Slide 51: ROM based controller

## Slide 52: ROM based controller
Think of new instructions that you can design with this datapath!
Notes: mv rd, rs
neg rd, rs
inc rd
abs rd, rs
li rd, imm
getpc rd
seqz rd, rs (rd ← (rs == 0) ? 1 : 0)
swp rs, imm(rd):
Mem[rd + imm] ← rs
rd ← rd + imm
pcadd rd, rs1
nop-store rs2, (rs1)